## Slide 1: RingGuard
AI Video Intelligence and Workplace Safety System
Sustainathon 2026 · VIT Bengaluru · Team Kraken
Every factory has cameras nobody watches.
Most AI adds a dashboard nobody watches.
Ours picks up the phone.
Notes: Open with the one-line pitch. RingGuard watches CCTV with AI, turns detections into confirmed incidents, and phones the right person within seconds.

## Slide 2: Abstract
RingGuard is an on-premise system that watches ordinary CCTV and phone cameras, detects safety events with computer vision, confirms them with a rules engine, and acts: it saves evidence, alerts the dashboard in under two seconds and phones the responsible guards with an escalation ladder. An AI voice agent, Friday, talks to the guard on the call, understands replies such as "I'm going", and answers spoken or typed questions about incidents. Video never leaves the site; only short alert text reaches cloud services. Custom YOLO11 models for fire, smoke, PPE and riders' helmets were trained on public datasets plus our own footage, and run on a laptop CPU through OpenVINO.
Keywords
Computer vision
YOLO11 + ByteTrack
Workplace safety
Fire & smoke detection
Face recognition
Conversational voice AI
Escalation
Edge AI / OpenVINO
On-premise privacy
Notes: Read the abstract in one breath: watch, confirm, act. Then point at the keywords; they map to the sections that follow.

## Slide 3: Cameras record everything, but nobody is watching
Recorded, not watched
CCTV is mostly used after an accident, to find out what happened. During a night shift a single guard may be responsible for dozens of screens.
Dashboards wait for someone
Most AI video tools add alerts to another screen. An alert on a screen nobody is looking at helps nobody at 2 a.m.
A ringing phone gets attention
RingGuard closes the loop: it confirms the event, finds the right person and calls them, then keeps escalating until someone responds.
Notes: The gap is not detection quality, it is response. Our design goal: the right human knows within seconds.

## Slide 4: Problem statement and objectives
The problem
Fires, falls, intruders in restricted areas and missing safety gear happen in seconds, but in most workplaces they are noticed late, by chance, or only on the recording afterwards. Existing alerts depend on someone watching a screen, and sending video to the cloud raises privacy and cost concerns.
1
Detect fire, smoke, falls, restricted entry, PPE, riders without helmets, crowding, unattended bags
2
Confirm turn single detections into incidents with rules, so one wrong frame never raises an alarm
3
Act fast dashboard in under 2 s, phone ringing in under 15 s, escalate until someone acknowledges
4
Talk a voice agent that speaks with the guard and answers questions about incidents
5
Stay private run on-premise on a laptop CPU: video and faces never leave the site
Notes: Problem on the left; five measurable objectives on the right. The numbers (2 s, 15 s) are our targets and we report against them in the results.

## Slide 5: Related work and where RingGuard differs
Approach | Detects events | Confirms with rules | Calls people | Talks back (voice AI) | Video stays on site
Conventional CCTV / NVR recording | ○ | ○ | ○ | ○ | ●
Cloud AI video analytics platforms | ● | ● | ○ | ○ | ○
Research fire / PPE detectors (YOLO, CNN) | ● | ○ | ○ | ○ | ●
Smoke detectors and alarm panels | ● | — | sometimes | ○ | ●
RingGuard (ours) | ● | ● | ● | ● | ●
● yes ○ no. Our contribution is not a new detector; it is the closed loop from camera to a confirmed incident to a conversation with the right person, on hardware a small site already owns.
Notes: Be fair to related work: detectors exist and cloud platforms exist. The gap we fill is the response loop and on-premise privacy, combined.

## Slide 6: System architecture
Cameras
Android phones (IP Webcam), laptop webcam, RTSP CCTV
Sensors (next)
ESP32 smoke sensor, panic button over HTTP
Badge / QR
Duty check-in, badge scans per area
Camera worker
one process per camera
Latest-frame capture
YOLO11-pose + ByteTrack
Fire/smoke · PPE · helmet
Face ID (YuNet + SFace)
Rules engine
Clip, snapshot, all-day MP4
Live MJPEG view (25 fps)
FastAPI core
local server
PostgreSQL
Incidents + audit
Escalation ladder
Roles & camera scope
WebSocket events
Signed media links
Friday assistant
Dashboard
React live grid, alarms, Friday
Phone calls
Twilio voice + WhatsApp
Cloud AI
Groq, Whisper, Rumik: text only
Video, faces and recordings stay on the laptop. Only short alert text leaves the site.
Notes: Walk left to right. Each camera has its own worker process, so one slow or crashed camera never affects another. The API never runs detection inside a request; workers report confirmed incidents to it.

## Slide 7: Technology stack
Vision
Ultralytics YOLO11n-pose · ByteTrack · custom YOLO11n fire/smoke, PPE, rider-helmet · OpenCV YuNet + SFace · OpenVINO (Intel CPU) · FFmpeg H.264
Backend
Python 3.11 · FastAPI · Uvicorn · SQLAlchemy 2 · Alembic · PostgreSQL · APScheduler · httpx · psutil
Calls & alerts
Twilio Voice (TwiML, speech + keypad gather, signed webhooks) · WhatsApp · ngrok · 1 call/s queue
AI assistant
Groq LLM (JSON mode, function calling) · Ollama llama3.2:3b offline · Groq Whisper / faster-whisper · Rumik Silk TTS · Vosk / openWakeWord "Hey Friday"
Frontend
React 19 · TypeScript · Vite · Tailwind · TanStack Query · framer-motion · three.js voice orb · WebSocket
Training & quality
Google Colab T4 · Roboflow datasets + Auto Label · pytest (300+ tests) · Playwright browser checks
Notes: Every model, library and API here is listed in docs/disclosures.md, as the event rules ask.

## Slide 8: Methodology: from pixels to a confirmed incident
1 · Capture
A thread reads the camera nonstop and keeps only the newest frame, so analysis is never behind.
2 · Detect & track
YOLO11-pose finds people, keypoints and stable track IDs; extra models find fire, smoke, PPE, helmets.
3 · Rules
Feet in a zone for N s; fire in N of the last N+3 frames; torso flat and hips dropped for 5 s; per-type cooldown.
4 · Incident
Snapshot, 10 s clip (5 s before, 5 s after), database row, then the API is told within ~2 s.
Design principle: a detection is not an alarm. Thresholds live in settings, so a site tunes sensitivity without code changes.
Notes: Stress the rules layer: the model may flicker or make a one-frame mistake. Requiring several sightings and a dwell time is what makes the alarm trustworthy.

## Slide 9: Methodology: training our own models
Fire & smoke
D-Fire (~21k images) + ~200 of our own lighter photos and no-flame photos
PPE
Construction-PPE: helmet and high-visibility vest
Rider helmet
984 images: helmet types vs bald / cap / bare head
Training pipeline
1
Roboflow: fork, upload, Auto Label, review
2
Colab T4: fine-tune YOLO11n, 480 px
3
Export to OpenVINO (~2× faster on Intel CPU)
4
Worker loads it; rules use FIRE_CONF / SMOKE_CONF
Lesson learned: a close-up lighter looked like smoke to a model trained on distant fires; adding our own labelled footage fixed it.
Faces: pretrained YuNet + SFace (no training). Enrollment keeps 128-number fingerprints, never photos.
Notes: Explain transfer learning: start from YOLO11n pretrained on COCO, fine-tune on the domain data. The lighter story shows why domain data matters.

## Slide 10: Methodology: who gets called, and when
0 s
Incident confirmed
Dashboard alarm, Friday speaks, Head Guard called, WhatsApp to Admin with snapshot
0–5 s
Admin called
At once if away; 5 s grace if the Admin is looking at the dashboard
5–10 s
Manager called
Ladder stops at the first acknowledgement, from any channel
45 s
Nobody answered
Every guard on shift gets a WhatsApp and a roll-call phone call
Critical
fire, fall, restricted entry at night
High
smoke, restricted entry (day), crowding, bag
Low
PPE, loitering: WhatsApp + 18:00 digest, no calls
Rider, no helmet
calls only the guard of that gate camera
Notes: Routing is by severity, not by type alone. Never auto-call fire services: a human orders that. Twilio places about one call per second, so a 20-guard roll call takes about 20 seconds.

## Slide 11: Implementation: a phone call that talks back
Live call, critical fire
Friday Hi Ravi, this is Friday from RingGuard. There's a fire on the shop floor near the loading bay. Where are you right now?
Ravi I'm at the gate, going there now.
Friday Go, Ravi! I've told everyone you're on the way. Please be careful.
System Incident acknowledged by Ravi via phone · ladder stopped · dashboard updated
LLM decides, code acts
Groq returns only {reply, action}; the action must be on the call's whitelist (ack, false alarm, connect admin, alert all…).
Instant on the obvious
"I'm going / on my way" is matched without the LLM and answered at once.
Safety rules
Critical incidents can only be acknowledged by phone, never closed. "Alert everyone" needs a spoken yes.
Voice & record
Rumik voice, Twilio speech recognition, every line saved under Conversations with the call audio.
Notes: The key safety idea: the language model never acts directly. It proposes an action from a fixed list, and our code checks permissions and severity rules before doing anything.

## Slide 12: Implementation: restricted areas with face recognition
Enroll with consent
5 webcam photos → YuNet finds the face → SFace makes a 128-number fingerprint. Photos are discarded.
Mark an area restricted
One click per camera on the Restricted areas page; tick who may enter.
Recognise on camera
Only for people standing inside a restricted area: cosine similarity ≥ 0.40 = that person.
On the live view
Yash (allowed)
no alert
unknown
access alarm
Privacy by design
Consent required to enroll
Fingerprints only, deletable in one click
Runs on the laptop; nothing sent out
Every change in the audit log
Notes: Measured on test photos: the same person scored 0.78 similarity, a different person 0.13, so the 0.40 threshold separates them well. Faces that cannot be seen still raise the alarm: no face, no entry.

## Slide 13: Implementation: the control room
Live grid + full screen
Signed MJPEG streams at 25 fps; click a camera to fill the screen.
Alarms that look different
Fire orange, smoke grey, no-helmet yellow, other emergencies red; spoken once.
Friday assistant
"Show me the fire", "summary for today", "call everyone" (with a spoken yes).
All-day recordings
5-minute MP4 files per camera, kept 7 days, jump to any incident.
Roles and delegation
Admin, Manager, Head Guard, Guard; each sees only their cameras.
Audit and conversations
Who did what, when, by which channel; every call transcript.
Notes: Switch to the live demo here: press Demo alert, show the alarm, the timeline and the phone ringing.

## Slide 14: Evaluation: model accuracy
Chart: Validation mAP50 (higher is better, 1.0 = perfect)
| Helmet (PPE) | Vest (PPE) | Smoke | Fire | Fire model (all)
mAP50 | 0.83 | 0.83 | 0.73 | 0.59 | 0.66
What mAP50 means
How well boxes match real objects, counting a box as right when it overlaps the truth by at least half.
Why fire is lower
Fire varies most (lighters, glow, sunsets); the rules need several sightings, so a weak frame never calls anyone.
Data
D-Fire, Construction-PPE and a 984-image helmet set, plus our own lighter and room footage.
Notes: Numbers are from the validation splits after training on Colab. Be honest that fire is the hardest class and explain how the rules compensate.

## Slide 15: Results: speed, reliability and privacy
8.1
analysed frames/s
one camera on a test video, CPU only, no GPU (target 8+)
< 2 s
incident to dashboard
design target; the alarm panel opens in about 0.2 s once the API is told
0.78 / 0.13
face similarity
same person vs different person (threshold 0.40)
300+
automated tests
rules, call ladder, conversations, faces, permissions, API
Verified end to end
Restricted entry with face recognition; fire alarm to phone call; caller acknowledgement over the phone stopping the ladder; recordings; full-screen camera view.
Honest limits
A phone takes 3–6 s to start ringing (carrier network). Without a GPU, one laptop serves 2–3 cameras. Some glowing smoke can look like fire; rules and the human on the call catch it.
Notes: 8.1 analysed fps was measured with a test video and OpenVINO; on the demo laptop it depends on load and power mode. Keep the honest limits slide: juries trust teams who know their limits.

## Slide 16: Conclusion
RingGuard turns existing cameras into a system that notices, confirms and calls the right person in seconds, on hardware a small site already owns, without sending video to the cloud.
Next
"Suspected fire" pre-alarm: instant amber warning, calls once confirmed
ESP32 smoke sensor to confirm what the camera sees
Per-camera model sets and a small GPU box for 20+ cameras
Notes: Close with the pitch line again: every factory has cameras nobody watches; ours picks up the phone. Then invite questions.

## Slide 17: References
Jocher G., Qiu J. Ultralytics YOLO11 (2024). github.com/ultralytics/ultralytics
Zhang Y. et al. ByteTrack: Multi-Object Tracking by Associating Every Detection Box. ECCV 2022
de Venâncio P. V. A. B., Lisboa A. C., Barbosa A. V. An automatic fire detection system based on deep convolutional neural networks for low-power, resource-constrained devices (D-Fire). Neural Computing and Applications, 2022
Ultralytics. Construction-PPE dataset. docs.ultralytics.com/datasets/detect/construction-ppe
Wu W., Peng H., Yu S. YuNet: A Tiny Millisecond-level Face Detector. Machine Intelligence Research, 2023
Zhong Y. et al. SFace: Sigmoid-Constrained Hypersphere Loss for Robust Face Recognition. IEEE TIP, 2021
Radford A. et al. Robust Speech Recognition via Large-Scale Weak Supervision (Whisper). ICML 2023
Intel OpenVINO toolkit · FastAPI · PostgreSQL · Twilio Voice and WhatsApp APIs · Groq API · Ollama · Rumik Silk · Roboflow · Google Colab
Full list of models, datasets, libraries, APIs and AI tools used: docs/disclosures.md in our repository
Notes: Disclosures cover every model, dataset, API and the AI tools used during development, as required by the event rules.